Demystifying the Thunderbots Firmware

---
Contents
- Hardware
- Firmware
- VHDL

---
Hardware
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Hardware
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
STM32F405RG Microcontroller
- ARM Cortex-M4 with FPU
- 168 MHz
- 1 MiB Flash program memory
- 192 kiB RAM
AVR/8051/PIC16
STM32F4
PC

---
Hardware
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
XC6SLX9 FPGA
- 9,152 logic cells
- 16 multipliers
- 576 kiB block RAM
- No Flash!

---
Questions about hardware?

---
Boot Sequence
1. Power-up→vectors→stm32_main (main/main.c)
2. init_chip (stm32lib/init.c): data, bss, exceptions, clocks
3. gpio_init (stm32lib/gpio.c): mode (I/O/AN/AF), speed, pull
4. vTaskStartScheduler (FreeRTOS)→main_task (main/main.c)
5. Initialize MCU peripherals (including USB for CDC ACM)
6. Check for new MCU firmware on SD card (upgrade/*.c)
   →Install and reboot
7. Send FPGA bitstream from SD card to FPGA (icb.c)
8. Initialize ICB to talk to FPGA (icb.c)
9. run_normal (main.c)
10. Kill everything and reboot/shutdown/bootload (main.c)

---
run_normal
1. Initialize more MCU peripherals
2. Initialize radio via FPGA (mrf.c+icb.c)
3. Initialize motors via FPGA (motors.c)
4. Initialize encoders and control loop
5. Initialize lateral position sensor (lps.c)
6. Initialize data logging to SD card (log.c+sdcard.c)
7. Run the robot (tick.c)

---
Questions about boot sequence?

---
Interlude: FreeRTOS: What?
- Free Real-Time Operating System
- http://freertos.org/
- Tasks
- Semaphores
- Mutexes
- Queues
- Events

---
Interlude: FreeRTOS: Why?
- Some tasks need exact timing:
  - 200 Hz control loop
- Some tasks need to respond to events fast:
  - Received radio packet
- Some tasks don’t:
  - Writing log data to SD card
  - Sending debug text over USB port

---
Interlude: FreeRTOS: Why?
Idea:
for (;;) {
  if (five_millis_passed())
    run_control_loop();
  if (radio_packet_ready())
    receive_and_process_packet();
  if (log_records_ready())
    write_log_record();
}

---
Interlude: FreeRTOS: Why?
Idea:
for (;;) {
  if (five_millis_passed())
    run_control_loop();
  if (radio_packet_ready())
    receive_and_process_packet();
  if (log_records_ready())
    write_log_record();
}
What if this takes 1 ms…
… this takes 3…
… and this takes 2?
1 + 3 + 2 = 6→next run_control_loop is 1 ms late!

---
Interlude: FreeRTOS: Why?
Fixed:
for (;;) {
  if (five_millis_passing_soon()) {
    wait_for_five_millis();
    run_control_loop();
  } else if (radio_packet_ready())
    receive_and_process_packet();
  else if (log_records_ready())
    write_log_record();
}
What if this takes 10 ms?

---
Interlude: FreeRTOS: Why?
Fixed:
for (;;) {
  if (five_millis_passing_soon()) {
    wait_for_five_millis();
    run_control_loop();
  } else if (radio_packet_ready())
    receive_and_process_packet();
  else if (log_records_ready())
    write_log_record();
}

---
Interlude: FreeRTOS: Why?
Fixed:
for (;;) {
  if (five_millis_passing_soon()) {
    wait_for_five_millis();
    run_control_loop();
  } else if (radio_packet_ready())
    receive_and_process_packet();
  else if (log_records_ready())
    write_log_record();
}
What if this takes 10 ms?

---
Interlude: FreeRTOS: Why?
Fixed:
for (;;) {
  if (five_millis_passing_soon()) {
    wait_for_five_millis();
    run_control_loop();
  } else if (radio_packet_ready())
    receive_and_process_packet();
  else if (writing_log_record())
    finish_write_log_record();
  else if (log_records_ready())
    start_write_log_record();
}

---
Interlude: FreeRTOS: Why?
Fixed:
for (;;) {
  if (five_millis_passing_soon()) {
    wait_for_five_millis();
    run_control_loop();
  } else if (radio_packet_ready())
    receive_and_process_packet();
  else if (writing_log_record())
    finish_write_log_record();
  else if (log_records_ready())
    start_write_log_record();
}
Waste of processor time
Messy and confusing

---
Interlude: FreeRTOS: Why?
Fixed:
void control_task(void) {
  for(;;) {
    wait_for_five_millis();
    run_control_loop();
  }
}
void receive_task(void) {
  for(;;) {
    wait_for_radio_packet();
    process_radio_packet();
  }
}
void log_task(void) {
  for(;;) {
    get_log_record();
    write_log_record();
  }
}
Run all three functions at the same time!

---
Interlude: FreeRTOS: Why?
Fixed:
void control_task(void) {
  for(;;) {
    wait_for_five_millis();
    run_control_loop();
  }
}
void receive_task(void) {
  for(;;) {
    wait_for_radio_packet();
    process_radio_packet();
  }
}
void log_task(void) {
  for(;;) {
    get_log_record();
    write_log_record();
  }
}
Run all three functions at the same time!
Impossible: only one microcontroller!

---
Interlude: FreeRTOS: How?
- Fake it!
- Each task has a priority.
- No task runnable→put CPU to sleep.
- One task runnable→run it.
- Two tasks runnable→run most important task.
- More important task wakes up→freeze current task to run new task.

---
Questions about FreeRTOS?

---
So what happens when I tell the robot to move?

---
Moving the Robot: Setup
1. MRFTest: Select “Move(Point)”, enter coordinates, and push “Execute”.
2. Packet goes out over radio.

---
Moving the Robot: Setup
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Setup
1. Packet arrives at radio on robot.
2. Radio sets interrupt wire 0 V→3.3 V.
3. FPGA sees interrupt wire high (mrf_interrupt.vhd).
4. FPGA reads INTSTAT from radio→indicates packet received (mrf_interrupt.vhd).
5. FPGA reads packet to RAM (mrf_receive.vhd).

---
Moving the Robot: Setup
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Setup
FPGA signals received packet (mrf_receive.vhd→interrupt_controller.vhd).
FPGA combines interrupt sources→asserts interrupt wire to microcontroller (interrupt_controller.vhd).
1. MCU sees interrupt wire go high.
2. MCU issues EXTI interrupt, handled by exti0_isr (icb.c).
3. ISR wakes up ICB IRQ task irq_task() (icb.c).

---
Moving the Robot: Setup
IRQ task asks FPGA to send pending IRQ flags (icb.c+interrupt_controller.vhd).
1. irq_task() sees radio receive interrupt flag, calls radio receive handler rx_isr() (mrf.c).
2. rx_isr() sends notification to radio receive task receive_task() (receive.c), asleep in mrf_receive() (mrf.c).
3. mrf_receive() asks FPGA to send radio packet (icb.c+mrf_receive.vhd).

---
Moving the Robot: Setup
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Setup
1. receive_task() decodes packet, calls primitive_start() (primitives/primitives.c).
2. primitive_start():
  1. Ends current primitive
  2. Disarms auto-kick
  3. Stops dribbler
  4. Resets control loop
  5. Calls move_start() (primitives/move.c)
move_start() remembers target position data.

---
Questions about starting a movement primitive?

---
Moving the Robot: Execution
MCU timers count encoder ticks.

---
Moving the Robot: Execution
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Execution
FPGA continuously reads IMU data (common/accelerometer.vhd, common/gyro.vhd).
  - This data is not currently used.

---
Moving the Robot: Execution
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Execution
Tick time (5 ms) arrives.
1. normal_task() (tick.c) wakes up.
2. normal_task() does some miscellaneous stuff.
3. normal_task() calls encoder_tick().
4. encoder_tick() (encoder.c) reads timers.
5. encoder_tick() computes current speeds of wheels.
6. normal_tick() calls primitive_tick() (primitives/primitive.c).
7. primitive_tick() calls dr_tick() (dr.c).

---
Moving the Robot: Execution
dr_tick():
  1. Turns wheel speeds into robot speed
  2. Rotates robot speed into primitive-relative¹ based on current angle
  3. Updates current position based on robot speed
primitive_tick() calls move_tick().
¹Most primitives measure position in a coordinate space relative to
the robot position and orientation when the primitive started running.

---
Moving the Robot: Execution
move_tick():
  1. Plans a trajectory (bangbang.c)
  2. Rotates the trajectory to be relative to the robot’s current orientation (physics.c)
  3. Passes the trajectory to apply_accel() (control.c)
apply_accel():
  1. Converts the accelerations into (x,y,θ) forces
  2. Converts the (x,y,θ) forces into wheel forces
  3. Passes the forces to apply_wheel_force() (control.c)

---
Moving the Robot: Execution
apply_wheel_force():
  1. Reads the battery voltage
  2. Converts wheel forces into wheel torques
  3. Converts wheel torques into relative motor voltages (offsets from motor back EMF)
  4. Estimates present motor back EMFs based on wheel speed from encoders
  5. Adds present back EMFs to voltage offsets to get absolute applied motor voltages
  6. Converts applied voltages to PWM duty cycles based on battery voltage and passes them to wheels_drive() (wheels.c)

---
Moving the Robot: Execution
1. wheels_drive() saves PWM duty cycles.
2. normal_task() calls wheels_tick().
3. wheels_tick():
  1. Checks and updates motor thermal model
  2. Calls motor_set() (motor.c), which encodes PWM into packet for transmission.
2. normal_task() calls motor_tick() (motor.c).
3. motor_tick() sends PWM values to FPGA (icb.c).

---
Moving the Robot: Execution
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Moving the Robot: Execution
1. FPGA reads motor Hall sensors and generates commutation pattern (common/motor_commutator.vhd).
2. FPGA generates PWM waveform at requested duty cycle (common/motor_pwm.vhd).
3. FPGA combines commutation pattern with PWM waveform to yield MOSFET drive waveforms (common/motor.vhd).
4. Drive waveforms go to gate drivers and FETs.

---
Moving the Robot: Execution
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
… and all that happens 200 times every second.
Questions about moving the robot?

---
Other Interesting Tick Functions
- feedback_tick() (feedback.c)
  - Sends information back to the computer
- breakbeam_tick_fast() (breakbeam.c)
  - Checks if laser cut by ball
- dribbler_tick() (dribbler.c)
  - Selects dribbler motor PWM value, checks and updates thermal model, and calls motor_set()

---
Other Interesting Tick Functions
charger_tick() (charger.c)
  1. Reads battery and capacitor voltage
  2. Decides whether to charge capacitor
  3. Computes PWM duty cycle for charging
  4. Configures MCU timer to output PWM waveform to MOSFET driver in boost regulator

---
Moving the Robot: Execution
Encoders
Motors
SD Card
Accelerometer
LPS + Breakbeam
STM32F4 MCU
XC6SLX9 FPGA
Gyroscope
Power Control
Radio
Chicker
ICB

---
Normal and Fast Ticks
- Normal: 200 Hz frequency (5 ms period)
  - Control loops and motors
  - Capacitor charging
  - Implemented as FreeRTOS task
- Fast: 8 kHz frequency (125 µs period)
  - Auto-kick breakbeam checking and firing
  - Lateral position sensor sampling
  - Implemented as hardware ISR

---
Sources of Information
- What does this function do?
  - Doxygen comments
- What’s the format of this ICB packet?
  - icb.h
- What’s the format of this radio packet?
  - Wiki→Electrical Resources→Radio Protocol→2013
- What does this peripheral register do?
  - STM32F4 reference manual
- What’s attached to this I/O pin?
  - KiCad schematic files

---
Final questions?